### Media Service "HGW 1031"

Operational freedom on site redefined

Wireless Mobile Operating Panel: The HGW 1031

| The wireless handheld panel HGW 1031 from SIGMATEK | With the HGW 1031, SIGMATEK introduces a wireless mobile operating panel to the market. Through data exchange via WLAN, the up to 25 m long cable is eliminated and the user has a new freedom for monitoring and operation direct on site. The mobile panel is equipped with a resistive 10.4" color touch screen and an EDGE2 Technology processor, which is also suitable for demanding visualizations. With its well-conceived design, the mobile panel in IP54 protection is comfortable to operate for both right and left-handers. Despite the integrated battery pack, the HGW 1031 weighs only 1,200 g and therefore ensures low-fatigue work. The battery pack enables up to 2 hours of continuous operation. In the next step, the wireless handheld panel will be equipped with an emergency stop function via WLAN. In view of Industry 4.0, the ergonomics of the machine or system is increased via the WLAN communication. The HGW 1031 is, as all other SIGMATEK systems are, also comfortably programmed with the all-in-one engineering tool LASAL. As the visualization tool, LASAL SCREEN thereby provides extensive libraries of display and design elements, alarm and event functions, as well as recipe management. Visit us at the SPS IPC Drives in Nuremberg: Hall 7, Stand 270 |  |
| --- | --- | --- |

| Corporate Data | SIGMATEK is counted among the leading manufacturers of complete automation systems for machine and plant manufacturing worldwide. In the 28-year history of the company, trend setting automation technologies were developed in close coordination with customer demands. With a product spectrum that meets all requirements from best asset cost to high-end applications, today practically any job requirement can be covered with serial products. In keeping with the company's philosophy, long-term availability is guaranteed. The scope of delivery extends from control and I/O systems, IPCs, HMIs, Motion Control and Safety to the all-in-one engineering tool LASAL with object oriented programming and the real-time Ethernet VARAN. New technologies are regularly tested for their applicability in the automation industry and implemented with the shortest "time-to-market" in innovative products. This guarantees a highly modern product spectrum from one source. In-house research, development and production ensure the Salzburg Company, with over 450 employees at its headquarters, a place at the forefront of automation technology. With offices in Germany, Switzerland, Great Britain, The United States and China as well as sales and service partners in the most important international industrial centers, SIGMATEK worldwide is always close to the customer. |
| --- | --- |

| Contact addresses: GERMANY SIGMATEK GMBH Marie-Curie-Straße 9 D-76829 Landau Tel.: +49 / 6341 / 9421-0 Fax: +49 / 6341 / 9421-21 E-Mail: office@sigmatek.de www.sigmatek-automation.com | Austria and all other countries SIGMATEK GmbH & Co KG SIGMATEK straße 1 A-5112 Lamprechtshausen Tel. +43 / 6274 / 4321-0 Fax: +43 / 6274 / 4321-18 E-Mail: office@sigmatek.at www.sigmatek-automation.com |
| --- | --- |
| For inquiries please contact: | Ingrid Traintinger Marketing Communication E-Mail: ingrid.traintinger@sigmatek.at |