### Media Service "S-DIAS Safety"

Seamlessly integrated or as stand-alone

S-DIAS Safety: Slim and Freely Programmable

| In the minimum variant, requires only 25 mm control cabinet width: the modular, freely programmable S-DIAS Safety system from SIGMATEK | For modular and intelligent machines, flexible and programmable Safety systems are a basic requirement. With the slim, modular system S-DIAS Safety, SIGMATEK offers an economic solution with which Safety functions can be flexible, easily and scalably implemented. The core of this system is the SCP 111 Safety controller. Combined with the safe digital mix module SDM 081 with six digital inputs and two digital outputs, a freely programmable mini Safety system – within a control cabinet width of only 25 mm – is provided. Functions such as emergency stop, door contact, light grid or operating mode select switch can be thereby implemented. Further Safety-oriented I/O modules are available in the S-DIAS portfolio for complex Safety applications: The SDI 101 with ten digital inputs, the STO 081 with eight short-circuit proof, digital outputs, the relay module SRO 021 with two relay outputs, as well as the SSI 021 for analysis of two absolute value encoder signals (up to 32 bits). The application is comfortably programmed in the graphic editor of the LASAL SAFETY Designer. In the integrated library, Safety function blocks based on PLCopen are provided – which include for example, emergency stop, two-hand control or guard locking. Designed for the highest Safety requirements (SIL 3, PL e, Cat. 4), the TÜV-certified Safety system can be fully integrated into the S-DIAS control system. The flexible combination of safe and function-oriented modules enables individual adaptation to customer requirements. S-DIAS Safety can however, be used as a stand-alone solution. SPS IPC Drives Hall 7, Stand 270 |
| --- | --- |

| Corporate Data | SIGMATEK is counted among the leading manufacturers of complete automation systems for machine and plant manufacturing worldwide. In the 28-year history of the company, trend setting automation technologies were and are developed in close coordination with customer demands. With a product spectrum that meets all requirements from best asset cost to high-end applications, today practically any job requirement can be covered with serial products. In keeping with the company's philosophy, long-term availability is guaranteed. The scope of delivery extends from control and I/O systems, IPCs, HMIs, Motion Control and Safety to the all-in-one engineering tool LASAL with object oriented programming and the real-time Ethernet VARAN. New technologies are regularly tested for their applicability in the automation industry and implemented with the shortest "time-to-market" in innovative products. This guarantees a highly modern product spectrum from one source. In-house research, development and production ensure the Salzburg Company, with over 450 employees worldwide, a place at the forefront of automation technology. With subsidiaries in Germany, Switzerland, Great Britain, the USA, China and Korea as well as sales and service partners in the most significant international industry centers, SIGMATEK is always near the customer world wide |
| --- | --- |

| Contact addresses: GERMANY SIGMATEK GMBH Marie-Curie-Straße 9 D-76829 Landau Tel. +49 / 6341 / 9421-0 Fax: +49 / 6341 / 9421-21 E-Mail: office@sigmatek.de www.sigmatek-automation.com | Austria and all other countries SIGMATEK GmbH & Co KG SIGMATEK straße 1 A-5112 Lamprechtshausen Tel. +43 / 6274 / 4321-0 Fax: +43 / 6274 / 4321-18 E-Mail: office@sigmatek.at www.sigmatek-automation.com |
| --- | --- |
| For inquiries please contact: | Edith Holzner Marketing Communication E-Mail: edith.holzner@sigmatek.at |