### Media Service “CP 311 & CP 312“

S-DIAS CPUs with Dual-Core Processor: CP 311 & CP 312

Strong CPU Performance for the DIN Rail

| High-performance S-DIAS CPU with dual-core EDGE2 Technology processor | SIGMATEK expands the control system S-DIAS with two processor units for demanding automation tasks. The CPU modules CP 311 and CP 312 convince with high-performance dual-core processors based on EDGE 2 Technology (2x 800 MHz). Both CPUs achieve high efficiency via the integrated zero-voltage proof RAM with a data volume of 256 MB (DDR3 RAM) and the internal microSD card (512 MB). In addition to the real-time clock, buffer battery and CAN, a USB host and USB OTG (On the Go) are also available. One Ethernet and two VARAN interfaces (CP 311) or two Ethernet and one VARAN interface (CP 312) are integrated – and all this on a width of only 37.5 mm. With the S-DIAS dual-core CPUs, up to 64 I/O modules can be powered and controlled. One processor core handles real-time and cyclic tasks. In the other core, background and additional system tasks as well as the Linux-based operating system runs. The high-performance CPUs are optimally suited for multi-CPU solutions in Industry 4.0 applications such as predictive maintenance. They are designed for process, visualization and motion tasks. Communication runs via the real-time Ethernet system VARAN with a bus speed of 100 Mbit/s. The individual I/O modules can be accessed within 1.12 µs. The voltage supply for the CPU and I/O modules is directly integrated into the modules. Industrial Mini I/O connectors meet the high demands for robustness and compactness. Using the 2-point contact principle and a stable lock, they provide an exact fitting and vibration proof connection. The CP 311 and CP 312 can be comfortably programmed with the engineering suite LASAL in accordance with 61131-3. SPS IPC Drives: Hall 7, Stand 270 |
| --- | --- |

| Corporate Data | SIGMATEK is counted among the leading manufacturers of complete automation systems for machine and plant manufacturing worldwide. In the 28-year history of the company, trend setting automation technologies were and are developed in close coordination with customer demands. With a product spectrum that meets all requirements from best asset cost to high-end applications, today practically any job requirement can be covered with serial products. In keeping with the company's philosophy, long-term availability is guaranteed. The scope of delivery extends from control and I/O systems, IPCs, HMIs, Motion Control and Safety to the all-in-one engineering tool LASAL with object oriented programming and the real-time Ethernet VARAN. New technologies are regularly tested for their applicability in the automation industry and implemented with the shortest "time-to-market" in innovative products. This guarantees a highly modern product spectrum from one source. In-house research, development and production ensure the Salzburg Company, with over 450 employees worldwide, a place at the forefront of automation technology. With subsidiaries in Germany, Switzerland, Great Britain, the USA, China and Korea as well as sales and service partners in the most significant international industry centers, SIGMATEK is always near the customer world wide |
| --- | --- |

| Contact addresses: GERMANY SIGMATEK GMBH Marie-Curie-Straße 9 D-76829 Landau Tel. +49 / 6341 / 9421-0 Fax: +49 / 6341 / 9421-21 E-Mail: office@sigmatek.de www.sigmatek-automation.com | Austria and all other countries SIGMATEK GmbH & Co KG SIGMATEK straße 1 A-5112 Lamprechtshausen Tel. +43 / 6274 / 4321-0 Fax: +43 / 6274 / 4321-18 E-Mail: office@sigmatek.at www.sigmatek-automation.com |
| --- | --- |
| For inquiries please contact: | Edith Holzner Marketing Communication E-Mail: edith.holzner@sigmatek.at |